## Slide 1: Hands On OpenCLTM
Simon McIntosh-Smith,
Tom Deakin
and James Price
Includes contributions from Tim Mattson (Intel) and Benedict Gaster (AMD/Qualcomm/UWE)
Released under the "attribution CC BY" creative commons license.

## Slide 2: Prof Simon McIntosh-Smith
Graduated as Valedictorian in Computer Science from Cardiff University in 1991.
Joined Inmos to work for David May FTS as a microprocessor architect.
Moved to Pixelfusion in 1999 – a high-tech start-up designing the first GPGPU, a many-core general purpose graphics processor.
Co-founded ClearSpeed in 2002 as Director of Architecture and Applications.
Joined the CS department at the University of Bristol in April 2009 to focus on High Performance Computing. Member of OpenCL standards body, Khronos, and OpenMP ARB.

## Slide 3: Dr James Price
Graduated from University of Bristol in 2018 with a PhD in high performance computing, and in 2012 with an MEng in Computer Science.
Autumn 2012 internship with Apple in the USA writing OpenCL.
Joined Simon McIntosh-Smith’s research group as a PhD student in Jan 2013 to investigate parallel programming environments for heterogeneous systems. Sponsored by Imagination Technologies.
Has ported numerous applications to OpenCL, and contributes to the OpenCL and SPIR-V standards.

## Slide 4: Dr Tom Deakin
Graduated from University of Bristol in 2018 with a PhD in high performance computing, and in 2012 with an MSci in Computer Science and Mathematics.
Author of the BabelStream benchmark (previously GPU-STREAM), and the Mega-{Sweep|Stream} benchmarks. Contributor to LANL’s SNAP mini-app.
Joined Simon McIntosh-Smith’s research group as a PhD student in Sep 2014 to investigate deterministic neutral particle transport methods. Sponsored by AWE.
Has ported numerous applications to OpenCL, and contributes to the OpenCL and OpenMP standards.

## Slide 5: Course materials (CC-BY)
https://github.com/UoB-HPC/opencl-training-slides
https://github.com/UoB-HPC/opencl-training-code
These may be updated during the course if necessary.
Code can be cloned to your own machines, or to the machine we’ll use for training: Isambard
git clone git@github.com:UoB-HPC/opencl-training-code.git

## Slide 6: Course materials
In addition to these slides, C++ API header files, a set of exercises, and solutions, it is useful to have:
OpenCL Reference Card
This card will help you keep track of the API as you do the exercises:
https://www.khronos.org/developers/reference-cards
The v1.2 spec is also very readable and recommended to have on-hand:
https://www.khronos.org/registry/cl/specs/opencl-1.2.pdf

## Slide 7: Setting up Opencl platforms

## Slide 8: Running on Windows
The AMD/NVIDIA GPU drivers come with the required runtime libraries
Intel runtime for CPU/GPU must be downloaded
The vendor SDKs provide the development headers and libraries:
  AMD APP SDK
  Intel INDE (Starter Edition)
  NVIDIA CUDA SDK
Or you can download the headers and source code for the OpenCL library (ICD loader) directly from Khronos

## Slide 9: Visual Studio
Your project must be configured to use the OpenCL development headers and library
In “Project Properties”:
  C/C++ >>> General >>> Additional Include Directories
    Add the path to the OpenCL include directory
    This will be somewhere in your SDK installation
    Contains CL directory, which contains cl.h
  Linker >>> General >>> Additional Library Directories
    Add the path to the OpenCL library directory
    This will be somewhere in your SDK installation
    Contains OpenCL.lib
  Linker >>> Input >>> Additional Dependencies
    Add OpenCL.lib
Some SDKs may provide templates to do this for you

## Slide 10: Running OSX?
OpenCL works out of the box!
Just compile your programs with
  -framework OpenCL
The Makefiles will use clang as the C compiler by default on Mac OS X
  Make sure you have the latest Xcode installed

## Slide 11: Some notes on setting up OpenCL
We will provide access to a machine with OpenCL implementations already installed
We also provide some instructions for setting up OpenCL on your machine for a variety of major platforms and device types
  AMD CPU, GPU and APU
  Intel CPU
  NVIDIA GPU
For the Linux setup slides we assume you are running 64-bit Ubuntu 12.04 LTS

## Slide 12: Setting up with AMD GPU
Install some required packages:
  sudo apt-get install build-essential linux-headers-generic debhelper dh-modaliases execstack dkms lib32gcc1 libc6-i386 opencl-headers
Download the driver from amd.com/drivers
  Select your GPU, OS, etc.
  Download the .zip
  Unpack this with unzip filename.zip
Create the installer
  sudo sh fglrx*.run --buildpkg Ubuntu/precise
Install the drivers
  sudo dpkg –i fglrx*.deb
Update your Xorg.conf file
  sudo amdconfig --initial --adapter=all
Reboot!
  Check all is working by running fglrxinfo
* Fglrx is the name of AMD’s graphics driver for the GPUs

## Slide 13: Setting up with AMD CPU
Download the AMD APP SDK from their website
Extract with tar -zxf file.tar.gz
Install with
  sudo ./Install*.sh
Create symbolic links to the library and includes
  sudo ln –s /opt/AMDAPP/lib/x86_64/* /usr/local/lib
  sudo ln –s /opt/AMDAPP/include/* /usr/local/include
Update linker paths
  sudo ldconfig
Reboot and run clinfo
  Your CPU should be listed

## Slide 14: Setting up with AMD APU
The easiest way is to follow the AMD GPU instructions to install fglrx.
This means you can use the CPU and GPU parts of your APU as separate OpenCL devices.
You may have to force your BIOS to use integrated graphics if you have a dedicated GPU too.

## Slide 15: Setting up with Intel CPU
NB: requires an Intel® Xeon™ processor on Linux
Download the Xeon Linux SDK from the Intel website
Extract the download
  tar -zxf download.tar.gz
Install some dependancies
  sudo apt-get install rpm alien libnuma1
Install them using alien
  sudo alien –i *base*.rpm *intel-cpu*.rpm *devel*.rpm
Copy the ICD to the right location
  sudo cp /opt/intel/<version>/etc/intel64.icd /etc/OpenCL/vendors/

## Slide 16: Setting up with Intel® Xeon Phi™
Intel® Xeon Phi™ coprocessor are specialist processor only found in dedicated HPC clusters.
As such, we expect most users will be using them in a server environment set up by someone else – hence we wont discusses setting up OpenCL on the Intel® Xeon Phi™ coprocessor in these slides
Once installed, they're very easy to target with OpenCL

## Slide 17: Setting up with NVIDIA GPUs
Blacklist the open source driver (IMPORTANT)
  sudo nano /etc/modprobe.d/blacklist.conf
  Add the line: blacklist nouveau
Install some dependencies
  sudo apt-get install build-essential linux-header-generic opencl-headers
Download the NVIDIA driver from their website and unpack the download
In a virtual terminal (Ctrl+Alt+F1), stop the windows manager
  sudo service lightdm stop
Give the script run permissions then run it
  chmod +x *.run
  sudo ./*.run
The pre-install test will fail – this is OK!
Say yes to DKMS, 32-bit GL libraries and to update your X config
Reboot!

## Slide 18: Installing pyopencl
Make sure you have python installed
Install the numpy library
  sudo apt-get install python-numpy
Download the latest version from the pyopencl website
  Extract the package with tar -zxf
Run to install as a local package
  python setup.py install --user

## Slide 19: C/C++ linking (gcc/g++)
In order to compile your OpenCL program you must tell the compiler to use the OpenCL library with the flag: –l OpenCL
If the compiler cannot find the OpenCL header files (it should do) you must specify the location of the CL/ folder with the –I (capital “i”) flag
If the linker cannot find the OpenCL runtime libraries (it should do) you must specify the location of the lib file with the –L flag

## Slide 20: Installable Client Driver (ICD)
The ICD allows you to choose between different OpenCL Platforms on a single machine
  I.e. run kernels on your CPU and an accelerator (GPU), or switching between Intel and AMD OpenCL implementations for the CPU
This means you can link your program against one OpenCL implementation, but run your code on a different one
The ICD Loader works out which runtime library to send your API calls to on your behalf so you don’t usually have to worry about this!
  When installing OpenCL it will usually put a file in /etc/OpenCL/vendors which contains the name of the library for that platform

## Slide 21: An overview of OpenCL

## Slide 22: It’s a Heterogeneous world
OpenCL lets Programmers write a single portable program that uses ALL resources in the heterogeneous platform
A modern computing platform may include:
One or more CPUs
One of more GPUs
DSP processors
Accelerators
FPGAs
… and more …
E.g. Intel® Core i7-8700K:
Six-core Coffee Lake x86 with Intel® UHD Graphics 630

## Slide 23: Processor trends
Individual processors have many (possibly heterogeneous) cores.
The Heterogeneous many-core challenge:
How are we to build a software ecosystem for the Heterogeneous many core platform?
Third party names are the property of their owners.
64 cores
16 wide SIMD
NVIDIA® Turing® RTX 8000
64 cores
64 wide SIMD
AMD® Vega
Intel® Xeon Phi™ (KNL) CPU
72 cores
64 wide SIMD
+ 576 Tensor Cores
+ 72 RT Cores
Notes: NVIDIA Turing RTX 8000 TU102: https://www.anandtech.com/show/13282/nvidia-turing-architecture-deep-dive/7

## Slide 24: Many-core performance potential
Notes: The CPU is 16 cores of Sandy Bridge at 3.1 GHz

## Slide 25: How do we unlock this potential?
Need efficient, expressive, parallel programming languages
Also need cross-platform standards
Ideally not just for HPC so that they have sufficient momentum for the long term
OpenCL is the only parallel programming language that meets all these many-core requirements today

## Slide 26: Industry Standards for Programming Heterogeneous Platforms
OpenCL – Open Computing Language
Open, royalty-free standard for portable, parallel programming of heterogeneous parallel computing CPUs, GPUs, and other processors
CPUs
Multiple cores driving performance increases
GPUs
Increasingly general purpose data-parallel computing
Graphics APIs and Shading Languages
Multi-processor programming – e.g. OpenMP
Emerging Intersection
Heterogeneous Computing

## Slide 27: The origins of OpenCL
AMD
ATI
NVIDIA
Intel
Apple
Merged, needed commonality across products
GPU vendor – wants to steal market share from CPU
CPU vendor – wants to steal market share from GPU
Was tired of recoding for many core, GPUs.
Pushed vendors to standardize.
Wrote a rough draft straw man API
Khronos Compute group formed
ARM
Nokia
IBM
Sony
Qualcomm
Imagination
TI
Third party names are the property of their owners.
+ many more

## Slide 28: OpenCL Working Group within Khronos
Diverse industry participation
  Processor vendors, system OEMs, middleware vendors, application developers.
OpenCL became an important standard upon release by virtue of the market coverage of the companies behind it.
Third party names are the property of their owners.

## Slide 29: OpenCL 2.2 Released November 2017
First launched Jun’08
6 months from “strawman” to OpenCL 1.0
Rapid innovation to match pace of hardware innovation
  Committed to backwards compatibility to protect software investments
2011
OpenCL 1.2
Becomes industry baseline for heterogeneous
parallel computing
OpenCL 2.1
SPIR-V 1.0
SPIR-V 1.1 in Core
Kernel Language Flexibility
OpenCL 2.2
SPIR-V 1.2
OpenCL C++ Kernel Language
Static subset of C++14
Templates and Lambdas
SPIR-V 1.2 in Core
OpenCL C++ support
Pipes Efficient device-scope communication between kernels
2017
2015
2013
OpenCL 2.0
Enables new class of hardware
SVM
Generic Addresses
On-device dispatch

## Slide 30: OpenCL: From cell phone to supercomputer
OpenCL Embedded profile for mobile and embedded silicon
  Relaxes some data type and precision requirements
  Avoids the need for a separate “ES” specification
Khronos APIs provide computing support for imaging & graphics
  Enabling advanced applications in, e.g., Augmented Reality
OpenCL will enable parallel computing in new markets
  Mobile phones, cars, avionics
A camera phone with GPS processes images to overlay generated images on surrounding scenery

## Slide 31: OpenCL Platform Model
One Host and one or more OpenCL Devices
  Each OpenCL Device is composed of one or more Compute Units
    Each Compute Unit is divided into one or more Processing Elements
Memory divided into host memory and device memory
Processing Element
OpenCL Device
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
Host
Compute Unit

## Slide 32: OpenCL Platform Example (One node, two CPU sockets, two GPUs)
CPUs:
Treated as one OpenCL device
  One CU per core
  1 PE per CU, or if PEs mapped to SIMD lanes, n PEs per CU, where n matches the SIMD width
Remember:
  the CPU will also have to be its own host!
GPUs:
Each GPU is a separate OpenCL device
Can use CPU and all GPU devices concurrently through OpenCL
CU = Compute Unit; PE = Processing Element

## Slide 33
Collaboration between GW4 Alliance (universities of Bristol, Bath, Cardiff, Exeter), the UK Met Office, Cray, and Arm
£3 million, funded by EPSRC
The first large-scale, Arm-based production supercomputer
Also contains 8 Intel Xeon Phi (KNL), 4 Intel Xeon nodes (Broadwell), and 8 NVIDIA P100 GPUs
OpenCL is installed for the CPUs and GPUs in Isambard

## Slide 34: Using Isambard (1/2)
# Log in to the Isambard bastion node
# This node acts as a gateway to the rest of the system
# You will be assigned an account ID (01, 02, …)
# Your password is openclNOV18
ssh br-trainXX@isambard.gw4.ac.uk
# Log in to Isambard Phase 1 from the bastion node
ssh phase1
# Change to directory containing the first exercise
cd opencl-training/exercises/DeviceInfo
# List files
ls
[br-train01@login-01 exercises]$ ls
deviceinfo.c deviceinfo.cpp DeviceInfo.vcxproj DeviceInfo.vcxproj.filters Makefile submit_deviceinfo
Job submission script
Exercise starting code

## Slide 35: Using Isambard (2/2)
# Build exercise
make
# Submit job
qsub submit_deviceinfo
# Check job status
qstat -u $USER
# Check output from job
# Output file will have the job identifier in name
# This will be different each time you run a job
cat deviceinfo.oXXXX
Job status:
Q = Queued
R = Running
C = Complete
(job will disappear shortly after completion)
Req'd Req'd Elap
Job ID Username Queue Jobname SessID NDS TSK Memory Time S Time
--------------- -------- -------- ---------- ------ --- --- ------ ----- - -----
9376.master.gw4 br-trai pascalq deviceinfo 154770 1 36 -- 00:02 R 00:00

## Slide 36: Exercise: Platform Information
Goal:
  Verify that you can run a simple OpenCL program.
Procedure:
  Take the provided DeviceInfo program, inspect it in the editor of your choice, build the program and run it.
Expected output:
  Information about the installed OpenCL platforms and the devices visible to them.
Extension:
  Run the command clinfo which comes as part of the AMD SDK but should run on all OpenCL platforms. This outputs all the information the OpenCL runtime can find out about devices and platforms.

## Slide 37: Exercise: Platform Information
[br-smcintoshsmith@pascal-002 DeviceInfo]$ more deviceinfo.o16094
Number of OpenCL platforms: 1
-------------------------
Platform: NVIDIA CUDA
Vendor: NVIDIA Corporation
Version: OpenCL 1.2 CUDA 9.1.84
Number of devices: 2
-------------------------
Name: Tesla P100-PCIE-16GB
Version: OpenCL C 1.2
Max. Compute Units: 56
Local Memory Size: 48 KB
Global Memory Size: 16280 MB
Max Alloc Size: 4070 MB
Max Work-group Total Size: 1024
Max Work-group Dims: ( 1024 1024 64 )
-------------------------
-------------------------
Name: Tesla P100-PCIE-16GB
Version: OpenCL C 1.2
Max. Compute Units: 56
Local Memory Size: 48 KB
Global Memory Size: 16280 MB
Max Alloc Size: 4070 MB
Max Work-group Total Size: 1024
Max Work-group Dims: ( 1024 1024 64 )
-------------------------
-------------------------
GPU

## Slide 38: Exercise: Platform Information
[br-smcintoshsmith@pascal-002 DeviceInfo]$ more deviceinfo.o16106
Number of OpenCL platforms: 1
-------------------------
Platform: Intel(R) CPU Runtime for OpenCL(TM) Applications
Vendor: Intel(R) Corporation
Version: OpenCL 2.1 LINUX
Number of devices: 1
-------------------------
Name: Intel(R) Xeon(R) CPU E5-2695 v4 @ 2.10GHz
Version: OpenCL C 2.0
Max. Compute Units: 36
Local Memory Size: 32 KB
Global Memory Size: 128823 MB
Max Alloc Size: 32205 MB
Max Work-group Total Size: 8192
Max Work-group Dims: ( 8192 8192 8192 )
-------------------------
-------------------------
CPU

## Slide 39: Exercise 1: Platform Information
Open the Visual Studio solution:
  exercises\Intro-Exercises.sln
(allow it to upgrade projects if prompted)
Select the DeviceInfo project
Build and run the project
Check that it finds your OpenCL device(s)

## Slide 40: Important OpenCL concepts

## Slide 41: OpenCL Platform Model
One Host and one or more OpenCL Devices
  Each OpenCL Device is composed of one or more Compute Units
    Each Compute Unit is divided into one or more Processing Elements
Memory divided into host memory and device memory
Processing Element
OpenCL Device
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
Host
Compute Unit

## Slide 42: The BIG idea behind OpenCL
Replace loops with functions (a kernel) executing at each point in a problem domain
  E.g., process an n element array with one kernel invocation per element
Traditional loops
Data Parallel OpenCL
void
mul(const int n,
const float *a,
const float *b,
float *c)
{
int i;
for (i = 0; i < n; i++)
c[i] = a[i] * b[i];
}
__kernel void
mul(__global const float *a,
__global const float *b,
__global float *c)
{
int i = get_global_id(0);
c[i] = a[i] * b[i];
}
// many instances of the kernel,
// called work-items, execute
// in parallel

## Slide 43: An N-dimensional domain of work-items
Global Dimensions:
  1024x1024 (whole problem space)
Local Dimensions:
  128x128 (work-group, executes together)
Choose the dimensions that are “best” for your algorithm
1024
1024
Synchronization between work-items possible only within work-groups:
barriers and memory fences
Cannot synchronize between work-groups within a kernel

## Slide 44: OpenCL N Dimensional Range (NDRange)
The problem we want to compute will have some dimensionality;
  E.g. compute a kernel on all points in a rectangle
When we execute the kernel we specify up to 3 dimensions
We also specify the total problem size in each dimension; this is called the global size
We associate each point in the iteration space with a work-item

## Slide 45: OpenCL N Dimensional Range (NDRange)
Work-items are grouped into work-groups; work-items within a work-group can share local memory and can synchronize
We can specify the number of work-items in a work-group; this is called the local size (or work-group size)
Or you can let the OpenCL run-time choose the work-group size for you (may not be optimal)

## Slide 46: OpenCL Memory model
Private Memory
  Per work-item
Local Memory
  Shared within a
  work-group
Global Memory / Constant Memory
  Visible to all
  work-groups
Host memory
  On the CPU
Memory management is explicit: You are responsible for moving data from
host → global → local and back

## Slide 47: The Memory Hierarchy
Private memory
O(10) words/WI
Local memory
O(1) KBytes/WG
Global memory
O(10) GBytes
Host memory
O(10-100) GBytes
Private memory
O(2-3) words/cycle/WI
Local memory
O(10) words/cycle/WG
Global memory
O(800-1,000) GBytes/s
Host memory
O(10) GBytes/s
Speeds and feeds approx. for a high-end discrete GPU, circa 2018
Bandwidths
Sizes

## Slide 48: Example: vector addition
The “hello world” program of data parallel programming is a program to add two vectors
C[i] = A[i] + B[i] for i=0 to N-1
For the OpenCL solution, there are two parts
  Kernel code
  Host code

## Slide 49: Vector Addition – C function
void vadd(const float *a,
const float *b,
float *c, int N)
{
for (int i=0; i<N; i++)
c[i] = a[i] + b[i];
}

## Slide 50: Vector Addition - Kernel
__kernel void vadd(__global const float *a,
__global const float *b,
__global float *c)
{
int i = get_global_id(0);
c[i] = a[i] + b[i];
}

## Slide 51: Vector Addition – Host
The host program is the code that runs on the host to:
  Setup the environment for the OpenCL program
  Create and manage kernels
5 main steps in all host programs:
  Define the platform … platform = devices+context+queues
  Create and build the program (dynamic library for kernels)
  Setup memory objects
  Define the kernel (attach arguments to kernel functions)
  Submit commands … transfer memory objects and execute kernels
As we go over the next set of slides, cross reference content on the slides to the reference card. This will help you get used to the reference card and how to pull information from the card and express it in code.

## Slide 52: The basic platform and runtime APIs in OpenCL (using C)
arg [0] value
arg [1] value
arg [2] value
arg [0] value
arg [1] value
arg [2] value
In Order
Queue
Out of Order
Queue
GPU
Context
__kernel void
dp_mul(global const float *a,
global const float *b,
global float *c)
{
int id = get_global_id(0);
c[id] = a[id] * b[id]; }
dp_mul
CPU program binary
dp_mul
GPU program binary
Programs
arg[0] value
arg[1] value
arg[2] value
Buffers
Images
In Order
Queue
Out of Order
Queue
Compute Device
GPU
CPU
dp_mul
Programs
Kernels
Memory Objects
Command Queues

## Slide 53: 1. Define the platform
Grab the first available platform:
  err = clGetPlatformIDs(1, &firstPlatformId,
  &numPlatforms);
Use the first CPU device the platform provides:
  err = clGetDeviceIDs(firstPlatformId,
  CL_DEVICE_TYPE_CPU, 1, &device_id, NULL);
Create a simple context with a single device:
  context = clCreateContext(firstPlatformId, 1,
  &device_id, NULL, NULL, &err);
Create a simple command-queue to feed our device:
  commands = clCreateCommandQueue(context, device_id,
  0, &err);

## Slide 54: Context and Command-Queues
Context:
  The environment within which kernels execute and in which synchronization and memory management is defined.
The context includes:
  One or more devices
  Device memory
  One or more command-queues
All commands for a device (kernel execution, synchronization, and memory transfer operations) are submitted through a command-queue.
Each command-queue points to a single device within a context.
Queue
Context
Device
Device Memory

## Slide 55: Command-Queues
Commands include:
  Kernel executions
  Memory object management
  Synchronization
The only way to submit commands to a device is through a command-queue.
Each command-queue points to a single device within a context.
Multiple command-queues can feed a single device.
  Used to define independent streams of commands that don’t require synchronization
Queue
Queue
Context
GPU
CPU

## Slide 56: Command-Queue execution details
Command queues can be configured in different ways to control how commands execute
In-order queues:
  Commands are enqueued and complete in the order they appear in the program (program-order)
Out-of-order queues:
  Commands are enqueued in program-order but can execute (and hence complete) in any order.
Execution of commands in the command-queue are guaranteed to be completed at synchronization points
  Discussed later
In practice, a single in-order command queue per device works well
Queue
Queue
Context
GPU
CPU

## Slide 57: 2. Create and Build the program
Define source code for the kernel-program as a string literal (OK for toy programs) or read from a file (for real applications).
Create the program object from your kernel source code:
  program = clCreateProgramWithSource(context, 1
  (const char**) &KernelSource, NULL, &err);
Compile the program to create a “dynamic library” from which specific kernels can be pulled:
  err = clBuildProgram(program, 0, NULL,NULL,NULL,NULL);

## Slide 58: Building Program Objects
__kernel void
horizontal_reflect(read_only image2d_t src,
write_only image2d_t dst)
{
int x = get_global_id(0); // x-coord
int y = get_global_id(1); // y-coord
int width = get_image_width(src);
float4 src_val = read_imagef(src, sampler,
(int2)(width-1-x, y));
write_imagef(dst, (int2)(x, y), src_val);
}
The program object encapsulates:
  A context
  The program kernel source or binary
  List of target devices and build options
The C API build process to create a program object:
  clCreateProgramWithSource()
  clCreateProgramWithBinary()
OpenCL uses runtime compilation … because in general you don’t know the details of the target device when you ship the program
Compile for GPU
Compile for CPU
GPU
code
CPU
code

## Slide 59: Error messages
Fetch and print error messages:
  if (err != CL_SUCCESS) {
  size_t len;
  char buffer[2048];
  clGetProgramBuildInfo(program, device_id,
  CL_PROGRAM_BUILD_LOG, sizeof(buffer), buffer, &len);
  printf(“%s\n”, buffer);
  }
Important to check all your OpenCL API error messages!
Easier in C++ with try/catch (see later)

## Slide 60: Conventions for naming buffers
It can get confusing about whether a host variable is just a regular C array or an OpenCL buffer
A useful convention is to prefix the names of your regular host C arrays with “h_” and your OpenCL buffers which will live on the device with “d_”

## Slide 61: 3. Setup Memory Objects
For vector addition we need 3 memory objects: one each for input vectors A and B, and one for the output vector C.
Create input vectors and assign values on the host:
  float h_a[N], h_b[N], h_c[N];
  for (i = 0; i < N; i++) {
  h_a[i] = rand() / (float)RAND_MAX;
  h_b[i] = rand() / (float)RAND_MAX;
  }
Define OpenCL memory objects:
  d_a = clCreateBuffer(context, CL_MEM_READ_ONLY,
  sizeof(float)*N, NULL, NULL);
  d_b = clCreateBuffer(context, CL_MEM_READ_ONLY,
  sizeof(float)*N, NULL, NULL);
  d_c = clCreateBuffer(context, CL_MEM_WRITE_ONLY,
  sizeof(float)*N, NULL, NULL);
Notes: Good to mention the convention for naming the host and device-side variables here, i.e. h_ and d_ etc.

## Slide 62: What do we put in device memory?
Memory Objects:
A handle to a reference-counted region of global memory.
There are two kinds of memory object
Buffer object:
  Defines a linear collection of bytes (“just a C array”).
  The contents of buffer objects are fully exposed within kernels and can be accessed using pointers
Image object:
  Defines a two- or three-dimensional region of memory.
  Image data can only be accessed with read and write functions, i.e. these are opaque data structures. The read functions use a sampler.
  Used when interfacing with a graphics API such as OpenGL. More on this later.

## Slide 63: Creating and manipulating buffers
Buffers are declared on the host as type: cl_mem
Arrays in host memory hold your original host-side data:
  float h_a[N], h_b[N];
Create the buffer (d_a), assign sizeof(float)*N bytes from “h_a” to the buffer and copy it into device memory:
  cl_mem d_a = clCreateBuffer(context,
  CL_MEM_READ_ONLY | CL_MEM_COPY_HOST_PTR,
  sizeof(float)*N, h_a, NULL);

## Slide 64: Creating and manipulating buffers
Other common memory flags include:
  CL_MEM_WRITE_ONLY, CL_MEM_READ_WRITE
  These are from the point of view of the device
Submit command to copy the result buffer back to host memory at “h_c”:
  CL_TRUE = blocking on host, CL_FALSE = non-blocking
  clEnqueueReadBuffer(queue, d_c, CL_TRUE,
  sizeof(float)*N, h_c,
  NULL, NULL, NULL);
Notes: "Blocking" is from the point of view of the *host* - most API calls can return immediately or can block until the command has actually executed on the device.

## Slide 65: 4. Define the kernel
Create a kernel object from the kernel function “vadd”:
  kernel = clCreateKernel(program, “vadd”, &err);
Attach arguments of the kernel function “vadd” to memory objects:
  err = clSetKernelArg(kernel, 0, sizeof(cl_mem), &d_a);
  err |= clSetKernelArg(kernel, 1, sizeof(cl_mem), &d_b);
  err |= clSetKernelArg(kernel, 2, sizeof(cl_mem), &d_c);

## Slide 66: 5. Enqueue commands
Write Buffers from host memory into global memory (as non-blocking operations from the host's point of view):
  err = clEnqueueWriteBuffer(commands, d_a, CL_FALSE,
  0, sizeof(float)*N, h_a, 0, NULL, NULL);
  err = clEnqueueWriteBuffer(commands, d_b, CL_FALSE,
  0, sizeof(float)*N, h_b, 0, NULL, NULL);
Enqueue the kernel for execution (note: in-order so OK):
  err = clEnqueueNDRangeKernel(commands, kernel, 1,
  NULL, &global, &local, 0, NULL, NULL);
Notes: Might not need the writes if when you created the buffers you already initialised them by copying host memory, i.e. with a flag like CL_MEM_USE_HOST_PTR. More on all this later when we discuss pinned memory.

## Slide 67: 5. Enqueue commands
Read back result (as a blocking operation). We have an in-order queue which assures the previous commands will have completed before this read can begin.
  err = clEnqueueReadBuffer(commands, d_c, CL_TRUE,
  sizeof(float)*N, h_c, 0, NULL, NULL);

## Slide 68: Vector Addition – Host Program
// Find number of platforms
err = clGetPlatformIDs(0, NULL, &numPlatforms);
// Get all platforms
cl_platform_id Platform[numPlatforms];
err = clGetPlatformIDs(numPlatforms, Platform, NULL);
// Find a device
for (i = 0; i < numPlatforms; i++) {
err = clGetDeviceIDs(Platform[i],DEVICE,1,&device_id,NULL);
if (err == CL_SUCCESS)
break;
}
// Create a context for 1 device
context = clCreateContext(0, 1, &device_id, NULL,NULL,&err);
// Create a command queue for our device
commands = clCreateCommandQueue(context, device_id, 0, &err);
// Create the compute program from the source buffer
program = clCreateProgramWithSource(context, 1,
(const char **) &KernelSource, NULL, &err);
// Build the program
err = clBuildProgram(program, 0, NULL, NULL, NULL, NULL);
// Create the input and output arrays in device memory
d_a = clCreateBuffer(context, CL_MEM_READ_ONLY,
sizeof(float) * N, NULL, NULL);
d_b = clCreateBuffer(context, CL_MEM_READ_ONLY,
sizeof(float) * N, NULL, NULL);
d_c = clCreateBuffer(context, CL_MEM_WRITE_ONLY,
sizeof(float) * N, NULL, NULL);
// Create the compute kernel from the program
ko_vadd = clCreateKernel(program, "vadd", &err);
// Set the four arguments to our compute kernel
err = clSetKernelArg(ko_vadd, 0, sizeof(cl_mem), &d_a);
err |= clSetKernelArg(ko_vadd, 1, sizeof(cl_mem), &d_b);
err |= clSetKernelArg(ko_vadd, 2, sizeof(cl_mem), &d_c);
// Write a and b vectors into device global memory
err = clEnqueueWriteBuffer(commands, d_a, CL_TRUE, 0,
sizeof(float) * N, h_a, 0, NULL, NULL);
err = clEnqueueWriteBuffer(commands, d_b, CL_TRUE, 0,
sizeof(float) * N, h_b, 0, NULL, NULL);
// Execute the kernel, let the run-time choose WG size
err = clEnqueueNDRangeKernel(commands, ko_vadd, 1, NULL,
&global, NULL, 0, NULL, NULL);
// Read back the results from device global memory
err = clEnqueueReadBuffer(commands, d_c, CL_TRUE, 0,
sizeof(float) * N, h_c, 0, NULL, NULL );

## Slide 69: Vector Addition – Host Program
// Create the compute kernel from the program
ko_vadd = clCreateKernel(program, "vadd", &err);
// Set the four arguments to our compute kernel
err = clSetKernelArg(ko_vadd, 0, sizeof(cl_mem), &d_a);
err |= clSetKernelArg(ko_vadd, 1, sizeof(cl_mem), &d_b);
err |= clSetKernelArg(ko_vadd, 2, sizeof(cl_mem), &d_c);
// Write a and b vectors into device global memory
err = clEnqueueWriteBuffer(commands, d_a, CL_TRUE, 0,
sizeof(float) * N, h_a, 0, NULL, NULL);
err = clEnqueueWriteBuffer(commands, d_b, CL_TRUE, 0,
sizeof(float) * N, h_b, 0, NULL, NULL);
// Execute the kernel, let the run-time choose WG size
err = clEnqueueNDRangeKernel(commands, ko_vadd, 1, NULL,
&global, NULL, 0, NULL, NULL);
// Read back the results from device global memory
err = clEnqueueReadBuffer(commands, d_c, CL_TRUE, 0,
sizeof(float) * N, h_c, 0, NULL, NULL );
// Find number of platforms
err = clGetPlatformIDs(0, NULL, &numPlatforms);
// Get all platforms
cl_platform_id Platform[numPlatforms];
err = clGetPlatformIDs(numPlatforms, Platform, NULL);
// Find a device
for (i = 0; i < numPlatforms; i++) {
err = clGetDeviceIDs(Platform[i],DEVICE,1,&device_id,NULL);
if (err == CL_SUCCESS)
break;
}
// Create a context for 1 device
context = clCreateContext(0, 1, &device_id, NULL,NULL,&err);
// Create a command queue for our device
commands = clCreateCommandQueue(context, device_id, 0, &err);
// Create the compute program from the source buffer
program = clCreateProgramWithSource(context, 1,
(const char **) &KernelSource, NULL, &err);
// Build the program
err = clBuildProgram(program, 0, NULL, NULL, NULL, NULL);
// Create the input and output arrays in device memory
d_a = clCreateBuffer(context, CL_MEM_READ_ONLY,
sizeof(float) * N, NULL, NULL);
d_b = clCreateBuffer(context, CL_MEM_READ_ONLY,
sizeof(float) * N, NULL, NULL);
d_c = clCreateBuffer(context, CL_MEM_WRITE_ONLY,
sizeof(float) * N, NULL, NULL);
2) Create and build the program
3) Define memory objects
4) Create and setup kernel
5) Execute commands: a) Write buffers to device b) Execute the kernel c) Read buffer back to host
It’s complicated, but most of this is “boilerplate” and the same for most codes.
1) Define the platform: Devices + Context + Queues

## Slide 70: Exercise: Running the Vadd kernel
Goal:
  To inspect and verify that you can run an OpenCL kernel
Procedure:
  Take the provided C Vadd program. It will run a simple kernel to add two vectors together.
  Look at the host code and identify the API calls in the host code. Compare them against the API descriptions on the OpenCL reference card.
  There are some helper files which time the execution, output device information neatly and check errors.
Expected output:
  A message verifying that the vector addition completed successfully

## Slide 71: Exercise: modifying an OpenCL program
Goal:
  To verify that you understand host and kernel code
Procedure:
  Start with a VADD program in C
    cd ~/opencl-training/exercises/VAdd
    make
    qsub submit_vadd
    Take a look at the code to see how it works
  Modify vadd.c to create additional buffer objects and assign them to vectors defined on the host
  Then chain multiple vadds, e.g. C=A+B; D=C+E; F=D+G.
  Once this works, change VADD to add 3 vectors together at a time instead of 2, i.e. D=A+B+C
Expected output:
  A message to standard output verifying that the chain of 4-operand vector additions produced the correct result

## Slide 72: Overview of OpenCL APIs

## Slide 73: Host programs can be verbose
OpenCL’s goal is extreme portability, so it exposes everything
Most of the host code is the same from one application to the next – this re-use makes the verbosity a non-issue.
Common API combinations can be packaged into functions, C++ or Python classes, or libraries to make the reuse more convenient.

## Slide 74: The C++ Interface
Khronos has defined a common C++ header file containing a high level interface to OpenCL, cl.hpp
This interface is dramatically easier to work with1
Key OpenCL C++ API features:
  Uses common defaults for the platform and command-queue, saving the programmer from extra coding for the most common use cases
  Simplifies the basic API by bundling key parameters with the objects rather than requiring verbose and repetitive argument lists
  Ability to “call” a kernel from the host, like a regular function
  Error checking can be performed with C++ exceptions
1 especially for C++ programmers…

## Slide 75: The OpenCL C++ API ref card
Useful to have the OpenCL C++ reference card to hand
Download it from the Khronos website:
http://www.khronos.org/files/OpenCLPP12-reference-card.pdf
Doxygen available here: http://github.khronos.org/OpenCL-CLHPP/

## Slide 76: 1. Create a context and queue
Grab a context using a device type:
  cl::Context
  context(CL_DEVICE_TYPE_DEFAULT);
Create a command queue for the first device in the context:
  cl::CommandQueue queue(context);

## Slide 77: 2. Create and Build the program
Define source code for the kernel-program either as a string literal (great for toy programs) or read it from a file (for real applications).
Create the program object and compile to create a “dynamic library” from which specific kernels can be pulled:
  cl::Program program(context, KernelSource, true);
“true” tells OpenCL to build (compile/link) the program object
KernelSource is a string … either statically set in the host program or returned from a function that loads the kernel code from a file.

## Slide 78: Compiler error messages
For most real programs we will want to catch and report kernel compilation errors. To do this, we add an additional catch clause:
  catch (cl::BuildError error)
  {
  // Recover compiler messages for first device
  // .first is the device, .second is the log
  std::string log = error.getBuildLog()[0].second;
  std::cerr << "Build failed:" << std::endl
  << log
  << std::endl;
  }
  catch (cl::Error error)
  {
  ...
  }

## Slide 79: Compiler error messages (1/2)
For most real programs we will want to catch and report kernel compilation errors. To do this, we need to use an explicit build step:
  Do NOT build the program with the constructor (i.e. do not set the last argument in the program constructor to true). Instead, use:
      cl::Program program(context, util::loadProgram("matmul.cl"));
  Explicitly build the program within a try block to catch the error exception:
      try
      {
      program.build();
      }
      catch (cl::Error error)
      {
      // If it was a build error then show the error
      if (error.err() == CL_BUILD_PROGRAM_FAILURE)
      {
      // Recover compiler message (see the next slide)
      }
      throw error;
      }

## Slide 80: Compiler error messages (2/2)
Compiled code is associated with a specific device … so we need a handle to reference the device
std::vector<cl::Device> devices;
devices = context.getInfo<CL_CONTEXT_DEVICES>();
In our programming, we’ve been using the default device which is the first one (devices[0]).
We need to query the program object to get the “BuildInfo”
  std::string built = program.getBuildInfo <CL_PROGRAM_BUILD_LOG>(devices[0]);
Now we can output the error compiler message
std::cerr << built << "\n";

## Slide 81: Compiler error messages: Complete Example
cl::Program program(context, util::loadProgram("matmul.cl"));
try
{
program.build();
}
catch (cl::Error error)
{
// If it was a build error then show the error
if (error.err() == CL_BUILD_PROGRAM_FAILURE)
{
std::vector<cl::Device> devices;
devices = context.getInfo<CL_CONTEXT_DEVICES>();
std::string built = program.getBuildInfo <CL_PROGRAM_BUILD_LOG>(devices[0]);
std::cerr << built << "\n";
}
throw error;
}

## Slide 82: 3. Setup Memory Objects
For vector addition we need 3 memory objects, one each for input vectors A and B, and one for the output vector C
Create input vectors and assign values on the host:
  std::vector<float> h_a(N), h_b(N), h_c(N);
  for (i = 0; i < N; i++) {
  h_a[i] = rand() / (float)RAND_MAX;
  h_b[i] = rand() / (float)RAND_MAX;
  }
Define OpenCL device buffers and copy from host buffers:
  cl::Buffer d_a(context, h_a.begin(), h_a.end(), true);
  cl::Buffer d_b(context, h_b.begin(), h_b.end(), true);
  cl::Buffer d_c(context, CL_MEM_WRITE_ONLY, sizeof(float)*N);

## Slide 83: Creating and manipulating buffers
Buffers are declared on the host as object type: cl::Buffer
Arrays in host memory hold your original host-side data:
  std::vector<float> h_a, h_b;
Create the device-side buffer (d_a), assign read only memory to hold the host array (h_a) and copy it into device memory:
  cl::Buffer d_a(context, h_a.begin(), h_a.end(), true);
Start_iterator and end_iterator for the container-holding host-side object
Stipulates that this is a read-only buffer

## Slide 84: Creating and manipulating buffers
The last argument sets the device's read/write access to the Buffer. true means “read only” while false (the default) means “read/write”.
Can use explicit copy commands to copy from the device buffer (in global memory) to host memory:
  cl::copy(queue, d_c, h_c.begin(), h_c.end());
Can also copy from host memory to global memory:
  cl::copy(queue, h_c.begin(), h_c.end(), d_c);

## Slide 85: 4. Define the kernel
Create a kernel functor for the kernels you want to be able to call in the program:
  cl::KernelFunctor
  <cl::Buffer, cl::Buffer, cl::Buffer>
  vadd(program, “vadd”);
This means you can ‘call’ the kernel as a ‘function’ in your host code to enqueue the kernel.
Must match the pattern of arguments to the kernel.
A previously created “program object” serving as a dynamic library of kernels
The name of the function used for the kernel
Variable name
Notes: Two different ways to deal with kernels – either define a kernel functor, or create a kernel object (discussed on next slide).

## Slide 86: Create a kernel (advanced)
If you want to query information about a kernel, you will need a kernel object too:
  cl::Kernel ko_vadd(program, “vadd”);
  or
  cl::Kernel ko_vadd
  = myKernelFunctor.getKernel();
Get the maximum size for a work-group:
  ::size_t local = ko_vadd.getWorkGroupInfo
  <CL_KERNEL_WORK_GROUP_SIZE>(Device::getDefault());
If we set the local dimension ourselves or accept the OpenCL runtime’s, we don’t need this step
We can use any work-group-info parameter from table 5.15 in the OpenCL 1.1 specification. The function will return the appropriate type.

## Slide 87: 5. Enqueue commands
Specify global (and optionally local) dimensions
  cl::NDRange global(1024)
  cl::NDRange local(64)
  If you don’t specify a local dimension, it is assumed as cl::NullRange, and the runtime picks a size for you
Enqueue the kernel for execution (note: non-blocking):
  vadd(cl::EnqueueArgs(queue, global), d_a, d_b, d_c);
Read back result (as a blocking operation). We use an in-order queue to ensure the previous commands are completed before the read can begin
  cl::copy(queue, d_c, h_c.begin(), h_c.end());
Notes: The cl::copy() commands are all blocking, there is no non-blocking version of them. The reason for this is that their implementations are making use of pinned memory via Map and Unmap (more on this later), and these have to be dealt with in a blocking fashion to make sure we don't break things.

## Slide 88: C++ Interface: setting up the host program
Enable OpenCL API Exceptions. Do this before including the header file
  #define CL_HPP_ENABLE_EXCEPTIONS
Specify the version of OpenCL that you wish to target. Do this before including the header file
  #define CL_HPP_TARGET_OPENCL_VERSION 120
  #define CL_HPP_MINIMUM_OPENCL_VERSION 120
Include key header files … both standard and custom
  #include <CL/cl2.hpp> // Khronos C++ Wrapper API
  #include <cstdio> // For C style
  #include <iostream> // For C++ style IO
  #include <vector> // For C++ vector types
Notes: See Appendix “C++ for C programmers” for more info on C++

## Slide 89: C++ interface: The vadd host program
#define N 1024
using namespace cl;
int main(void) {
vector<float> h_a(N), h_b(N), h_c(N);
// initialize these host vectors…
Buffer d_a, d_b, d_c;
Context context(CL_DEVICE_TYPE_DEFAULT);
CommandQueue queue(context);
Program program(context,
loadprogram(“vadd.cl”), true);
// Create the kernel functor
KernelFunctor<Buffer, Buffer, Buffer>
vadd(program, “vadd”);
// Create buffers
// True indicates CL_MEM_READ_ONLY
// False indicates CL_MEM_READ_WRITE
d_a = Buffer(context, h_a.begin(), h_a.end(), true);
d_b = Buffer(context, h_b.begin(), h_b.end(), true);
d_c = Buffer(context, CL_MEM_WRITE_ONLY,
sizeof(float) * N);
// Enqueue the kernel
vadd(EnqueueArgs(queue, NDRange(N)),
d_a, d_b, d_c);
copy(queue, d_c, h_c.begin(), h_c.end());
}
Note: The default context and command queue are used when we do not specify one in the function calls. The code here also uses the default device, so these cases are the same.

## Slide 90: The C++ Buffer Constructor
The API definition:
  Buffer(startIterator, endIterator, bool readOnly, bool useHostPtr)
The readOnly boolean specifies whether the memory is CL_MEM_READ_ONLY (true) or CL_MEM_READ_WRITE (false)
  You must specify a true or false here
The useHostPtr boolean is false by default
  Therefore the array defined by the iterators is implicitly copied into device memory
  If you specify true:
    The memory specified by the iterators must be contiguous
    The context uses the pointer to the host memory, which becomes device accessible - this is the same as CL_MEM_USE_HOST_PTR
    The array might not be copied to device memory
We can also specify a context to use as the first argument in this API call

## Slide 91: The C++ Buffer Constructor
When using the buffer constructor which uses C++ vector iterators, remember:
  This is a blocking call
  The constructor will enqueue a copy to the first Device in the context (when useHostPtr == false)
  The OpenCL runtime will automatically ensure the buffer is copied across to the actual device you enqueue a kernel on later if you enqueue the kernel on a different device within this context

## Slide 92: The Python Interface
A Python library by Andreas Klöckner from University of Illinois at Urbana-Champaign
This interface is dramatically easier to work with1
Key features:
  Helper functions to choose platform/device at runtime
  getInfo() methods are class attributes – no need to call the method itself
  Call a kernel as a method
  Multi-line strings – no need to escape new lines!
1 not just for Python programmers…

## Slide 93: Setting up the host program
Import the pyopencl library
  import pyopencl as cl
Import numpy to use arrays etc.
  import numpy
Some of the examples use a helper library to print out some information
  import deviceinfo

## Slide 94
N = 1024
# create context, queue and program
context = cl.create_some_context()
queue = cl.CommandQueue(context)
kernelsource = open(‘vadd.cl’).read()
program = cl.Program(context, kernelsource).build()
# create host arrays
h_a = numpy.random.rand(N).astype(float32)
h_b = numpy.random.rand(N).astype(float32)
h_c = numpy.empty(N).astype(float32)
# create device buffers
mf = cl.mem_flags
d_a = cl.Buffer(context, mf.READ_ONLY | mf.COPY_HOST_PTR, hostbuf=h_a)
d_b = cl.Buffer(context, mf.READ_ONLY | mf.COPY_HOST_PTR, hostbuf=h_b)
d_c = cl.Buffer(context, mf.WRITE_ONLY, h_c.nbytes)
# run kernel
program.vadd(queue, h_a.shape, None, d_a, d_b, d_c)
# return results
cl.enqueue_copy(queue, h_c, d_c)

## Slide 95: We have now covered the basic platform runtime APIs in OpenCL
arg [0] value
arg [1] value
arg [2] value
arg [0] value
arg [1] value
arg [2] value
In Order
Queue
Out of Order
Queue
GPU
Context
__kernel void
dp_mul(global const float *a,
global const float *b,
global float *c)
{
int id = get_global_id(0);
c[id] = a[id] * b[id]; }
dp_mul
CPU program binary
dp_mul
GPU program binary
Programs
arg[0] value
arg[1] value
arg[2] value
Buffers
Images
In Order
Queue
Out of Order
Queue
Compute Device
GPU
CPU
dp_mul
Programs
Kernels
Memory Objects
Command Queues

## Slide 96: Exercise: Chaining vector add kernels
Goal:
  To verify that you understand manipulating kernel invocations and buffers in OpenCL's C++ API
Procedure:
  Start with a VADD program in C++
  Create additional buffer objects and assign them to vectors defined on the host (see the provided vadd programs for examples of how to do this)
  Chain vadds … e.g. C=A+B; D=C+E; F=D+G.
  Read back the final result and verify that it is correct
Expected output:
  A message to standard output verifying that the chain of vector additions produced the correct result
(Sample solution is for C = A + B; D = C + E; F = D + G; return F)

## Slide 97: Introduction to OpenCL kernel programming

## Slide 98: OpenCL C for Compute Kernels
Derived from ISO C99
  Restrictions: no recursion, function pointers, functions in C99 standard headers ...
  Preprocessing directives defined by C99 are supported (#include, #if etc.)
Built-in data types
  Scalar and vector data types, pointers
  Data-type conversion functions:
    convert_type<_sat><_roundingmode>
  Image types:
    image2d_t, image3d_t and sampler_t

## Slide 99: OpenCL C for Compute Kernels
Built-in functions — mandatory
  Work-Item functions, math.h, read/write images
  Relational, geometric functions, synchronization functions
  printf (OpenCL v1.2 or later)
Built-in functions — optional “extensions”
  Double precision, atomics to global and local memory
  Selection of rounding modes, writes to image3d_t surface

## Slide 100: OpenCL C Language Highlights
Function qualifiers
  __kernel qualifier declares a function as a kernel
    I.e. makes it visible to host code so it can be enqueued
  Kernels can call other (non kernel) device-side functions
Address space qualifiers
  __global, __local, __constant, __private
  Pointer kernel arguments must have an address space qualifier
Work-item functions
  get_global_id(), get_local_id(), get_group_id() etc.
Synchronization functions
  Barriers - all work-items within a work-group must execute the barrier function before any work-item can continue
  Memory fences - provides ordering between memory operations
Notes: Can leave off the double underscore prefixes on the OpenCL C qualifiers, i.e. kernel, global etc.

## Slide 101: OpenCL C Language Restrictions
Pointers to functions are not allowed
Pointers to pointers allowed within a kernel, but not as an argument to a kernel invocation
Bit-fields are not supported
Variable length arrays and structures are not supported
Recursion is not supported (yet!)
Double types are optional in OpenCL v1.1, but the key word is reserved
(note: most implementations support double)

## Slide 102: Worked example: Linear Algebra
1 | 2 | 1 | x |  | 1
1 | 3 | 3 | y | = | 2
1 | 1 | 4 | z |  | 6
Definition:
  The branch of mathematics concerned with the study of vectors, vector spaces, linear transformations and systems of linear equations.
Example: Consider the following system of linear equations
x + 2y + z = 1
x + 3y + 3z = 2
x + y + 4z = 6
  This system can be represented in terms of vectors and a matrix as the classic “Ax = b” problem.

## Slide 103: Solving Ax=b
1 | 0 | 0 |  | 1 | 2 | 1 |  | 1 | 2 | 1
1 | 1 | 0 |  | 0 | 1 | 2 | = | 1 | 3 | 3
1 | -1 | 1 |  | 0 | 0 | 5 |  | 1 | 2 | 4
LU Decomposition:
  transform a matrix into the product of a lower triangular and upper triangular matrix. It is used to solve a linear system of equations.
L
A
U
=
We solve for x, given a problem Ax=b
  Ax=b LUx=b
  Ux=(L-1)b x = (U-1)(L-1)b
So we need to be able to do matrix multiplication

## Slide 104: Matrix multiplication: sequential code
void mat_mul(int N, float *A, float *B, float *C)
{
int i, j, k;
for (i = 0; i < N; i++) {
for (j = 0; j < N; j++) {
C[i*N+j] = 0.0f;
for (k = 0; k < N; k++) {
// C(i, j) = sum(over k) A(i,k) * B(k,j)
C[i*N+j] += A[i*N+k] * B[k*N+j];
}
}
}
}
We calculate C=AB, where all three matrices are NxN
=
x
A(i,:)
B(:,j)
C(i,j)
Dot product of a row of A and a column of B for each element of C

## Slide 105: Matrix multiplication performance
Serial C code on CPU (single core).
Case | GFLOP/s | 
 | CPU | GPU
Sequential C (not OpenCL) | 0.85 | N/A
Device is 2x Intel® Xeon® CPU, E5-2695 v4 @ 2.1GHz (36 cores total) using gcc v6.1.
Third party names are the property of their owners.
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.
Notes: These are the Broadwell CPU nodes in Isambard phase 1. These same CPU nodes host the NVIDIA P100 GPUs.

## Slide 106: Matrix multiplication: OpenCL kernel (1/2)
__kernel void mat_mul(const int N, __global float *A, __global float *B, __global float *C)
{
int i, j, k;
for (i = 0; i < N; i++) {
for (j = 0; j < N; j++) {
C[i*N+j] = 0.0f;
for (k = 0; k < N; k++) {
// C(i, j) = sum(over k) A(i,k) * B(k,j)
C[i*N+j] += A[i*N+k] * B[k*N+j];
}
}
}
}
Mark as a kernel function and specify memory qualifiers

## Slide 107: Matrix multiplication: OpenCL kernel (2/2)
__kernel void mat_mul(const int N, __global float *A, __global float *B, __global float *C)
{
int i, j, k;
i = get_global_id(0);
j = get_global_id(1);
C[i*N+j] = 0.0f;
for (k = 0; k < N; k++) {
// C(i, j) = sum(over k) A(i,k) * B(k,j)
C[i*N+j] += A[i*N+k] * B[k*N+j];
}
}
}
}
Unroll the two outermost loops, instead setting loop indices i and j to be the global ids in the x and y direction

## Slide 108: Matrix multiplication: OpenCL kernel
__kernel void mat_mul(const int N, __global float *A, __global float *B, __global float *C)
{
int i, j, k;
i = get_global_id(0);
j = get_global_id(1);
C[i*N+j] = 0.0f;
for (k = 0; k < N; k++) {
// C(i, j) = sum(over k) A(i,k) * B(k,j)
C[i*N+j] += A[i*N+k] * B[k*N+j];
}
}
Tidy up a bit

## Slide 109: Matrix multiplication: OpenCL kernel improved
__kernel void mmul(
const int N,
__global float *A,
__global float *B,
__global float *C)
{
int k;
int i = get_global_id(0);
int j = get_global_id(1);
float tmp = 0.0f;
for (k = 0; k < N; k++)
tmp += A[i*N+k]*B[k*N+j];
C[i*N+j] = tmp;
}
Rearrange and use a local scalar for intermediate C element values (a common optimization in matrix multiplication functions)

## Slide 110: Matrix multiplication host program (C++ API)
// Setup the buffers, initialize matrices,
// and write them into global memory
cl::Buffer d_a(context, begin(h_A), end(h_A), true);
cl::Buffer d_b(context, begin(h_B), end(h_B), true);
cl::Buffer d_c(context, CL_MEM_WRITE_ONLY,
sizeof(float) * size);
cl::KernelFunctor
<int,cl::Buffer, cl::Buffer, cl::Buffer>
naive(program, "mmul");
zero_mat(N, h_C);
start_time = wtime();
naive(cl::EnqueueArgs(queue, cl::NDRange(N, N)),
N, d_a, d_b, d_c);
run_time = wtime() - start_time;
cl::copy(queue, d_c, begin(h_C), end(h_C));
results(N, h_C, run_time);
}
int main(int argc, char *argv[])
{
std::vector<float> h_A, h_B, h_C; // matrices
int N; // A[N][N],B[N][N],C[N][N]
int i, err;
int size; // num elements in each matrix
double start_time, run_time; // timing data
cl::Program program;
N = ORDER;
size = N*N;
h_A = std::vector<float>(size);
h_B = std::vector<float>(size);
h_C = std::vector<float>(size);
initmat(N, h_A, h_B, h_C);
// Compile for first kernel to setup program
program = cl::Program(C_elem_KernelSource, true);
Context context(CL_DEVICE_TYPE_DEFAULT);
cl::CommandQueue queue(context);
std::vector<Device> devices =
context.getInfo<CL_CONTEXT_DEVICES>();
cl::Device device = devices[0];
std::string s =
device.getInfo<CL_DEVICE_NAME>();
std::cout << "\nUsing OpenCL Device ”
<< s << "\n";
Setup buffers and write A and B matrices to the device memory
Declare and initialize data
Setup the platform and build program
Note: To use the default context/queue/device, skip this section and remove the references to context, queue and device.
Run the kernel and collect results
Create the kernel functor

## Slide 111: Matrix multiplication performance
Matrices are stored in global memory.
All the following results are from running C host code
Case | GFLOP/s | 
 | CPU | GPU
Sequential C (not OpenCL) | 0.85 | N/A
C(i,j) per work-item, all global | 111.8 | 70.3
Device is NVIDIA® Tesla® P100 GPU with 56 compute units, 3,584 PEs, CUDA 9.1.84
Device is 2x Intel® Xeon® CPU, E5-2695 v4 @ 2.1GHz
Third party names are the property of their owners.
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.

## Slide 112: Exercise: Matrix Multiplication
Goal:
  To write your first OpenCL kernel “from scratch”
  To multiply a pair of matrices
Procedure:
  cd ~/opencl-training/exercises/MatMul
  Start with the matrix multiplication serial code in matrix_lib.c and port this to a naïve kernel using the provided stub in kernel.cl
  We provide an OpenCL host program including the function to generate matrices and test results
  Verify the results
Expected output:
  A message to standard output verifying that the matrix multiply results are correct
  Report the runtime and the GFLOP/s

## Slide 113: Understanding the OpenCL memory hierarchy

## Slide 114: Optimizing matrix multiplication
MM cost determined by FLOP/s and memory movement:
  2*n3 = O(n3) FLOP/s
  Operates on 3*n2 = O(n2) numbers
To optimize matrix multiplication, we must ensure that for every memory access we execute as many FLOP/s as possible.
Outer product algorithms are faster, but for pedagogical reasons, let’s stick to the simple dot-product algorithm.
We will work with work-item/work-group sizes and the memory model to optimize matrix multiplication
=
x
A(i,:)
B(:,j)
C(i,j)
Dot product of a row of A and a column of B for each element of C

## Slide 115: An N-dimensional domain of work-items
Global Dimensions:
  1024x1024 (whole problem space)
Local Dimensions:
  128x128 (work-group, executes together)
Choose the dimensions that are “best” for your algorithm
1024
1024
Synchronization between work-items possible only within work-groups:
barriers and memory fences
Cannot synchronize between work-groups within a kernel

## Slide 116: OpenCL Memory model
Private Memory
  Per work-item
Local Memory
  Shared within a
  work-group
Global / Constant Memory
  Visible to all
  work-groups
Host memory
  On the CPU
Memory management is explicit: You are responsible for moving data from
host → global → local and back

## Slide 117: OpenCL Memory model
Private Memory
  Fastest & smallest: O(10) words/WI
Local Memory
  Shared by all WI’s in a work-group
  But not shared between work-groups!
  O(1-10) KBytes per work-group
Global / Constant Memory
  O(1-10) GBytes of Global memory
  O(10-100) KBytes of Constant memory
Host memory
  On the CPU - GBytes
Memory management is explicit: O(1-10) GBytes/s bandwidth to discrete GPUs for
Host <-> Global transfers

## Slide 118: Private Memory
Managing the memory hierarchy is one of the most important things to get right to achieve good performance
Private Memory:
  A very scarce resource, only a few tens of (32-bit) words per work-item at most
  If you use too much it spills to global memory or reduces the number of Work-Items that can be run at the same time, potentially harming performance*
  Think of these like registers on the CPU
* Occupancy on a GPU

## Slide 119: Local Memory*
Tens of KBytes per Compute Unit
  As multiple Work-Groups will be running on each Compute Unit, this means only a fraction of the total Local Memory size is available to each Work-Group
Assume O(1-10) KBytes of Local Memory per Work-Group
  Your kernels are responsible for transferring data between Local and Global/Constant memories. There are optimized library functions to help
  E.g. async_work_group_copy(), async_work_group_strided_copy(), …
Use Local Memory to hold data that can be reused by all the work-items in a work-group
Access patterns to Local Memory affect performance in a similar way to accessing Global Memory
  Have to think about things like coalescence & bank conflicts
* Typical figures for a discrete GPU

## Slide 120: Local Memory
Local Memory doesn’t always help…
  CPUs don’t have special hardware for it
  This can mean excessive use of Local Memory might slow down kernels on CPUs
  GPUs now have effective on-chip caches which can provide much of the benefit of Local Memory but without programmer intervention
  So, your mileage may vary!

## Slide 121: The Memory Hierarchy
Private memory
O(10) words/WI
Local memory
O(1) KBytes/WG
Global memory
O(10) GBytes
Host memory
O(10-100) GBytes
Private memory
O(2-3) words/cycle/WI
Local memory
O(10) words/cycle/WG
Global memory
O(800-1,000) GBytes/s
Host memory
O(10) GBytes/s
Speeds and feeds approx. for a high-end discrete GPU, circa 2018
Bandwidths
Sizes

## Slide 122: Memory Consistency
OpenCL uses a relaxed consistency memory model; i.e.
  The state of memory visible to a work-item is not guaranteed to be consistent across the collection of work-items at all times.
For each work-item:
  Memory has load/store consistency to the work-item’s private view of memory, i.e. it sees its own reads and writes correctly
Between work-items in a work-group:
  Local memory is consistent at a barrier.
Global memory is consistent within a work-group at a barrier, but not guaranteed across different work-groups!!
  This is a common source of bugs!
Consistency of memory shared between commands (e.g. kernel invocations) is enforced by synchronization (barriers, events, in-order queue)

## Slide 123: Work-Item Synchronization
Within a work-group:
  void barrier()
  Takes optional flags
  CLK_LOCAL_MEM_FENCE and/or CLK_GLOBAL_MEM_FENCE
  A work-item that encounters a barrier() will wait until ALL work-items in its work-group reach the barrier()
  Corollary: If a barrier() is inside a branch, then the branch must be uniform, i.e. taken by either:
    ALL work-items in the work-group, OR
    NO work-item in the work-group
Between different work-groups:
  No guarantees as to where and when a particular work-group will be executed relative to other work-groups
  Cannot exchange data, or have barrier-like synchronization between two different work-groups! (Critical issue!)
  Only solution: finish executing the kernel and start executing another
Ensure correct order of memory operations to local or global memory (with flushes or queuing a memory fence)
Notes: These barriers have been renamed as "work-group barriers" in OpenCL 2.0 to help clear up the confusion…
All this means, for example, that you couldn't transpose an image in global memory then reload and start processing that image all in one kernel. Have to finish one kernel after the global memory writes then start another to ensure all the global memory writes have completed before starting the global memory (re)reads.

## Slide 124: Optimizing matrix multiplication
There may be significant overhead to manage work-items and work-groups.
So let’s try having each work-item compute a full row of C
=
x
A(i,:)
B(:,j)
C(i,j)
Dot product of a row of A and a column of B for each element of C

## Slide 125: An N-dimension domain of work-items
Global Dimensions: 1024 (1D)
Whole problem space (index space)
Local Dimensions: leave to the run-time
Important implication: we will have a lot fewer work-items and work-groups. Why might this matter?
1024

## Slide 126: Reduce work-item overhead
__kernel void mmul(const int N,
__global float *A, __global float *B, __global float *C)
{
int k, j;
int i = get_global_id(0);
float tmp;
for (j = 0; j < N; j++) {
// N is width of rows in C
tmp = 0.0f;
for (k = 0; k < N; k++)
tmp += A[i*N+k] * B[k*N+j];
C[i*N+j] = tmp;
}
}
Do a whole row of C per work-item

## Slide 127: Matrix multiplication host program (C++ API)
// Setup the buffers, initialize matrices,
// and write them into global memory
cl::Buffer d_a(context, begin(h_A), end(h_A), true);
cl::Buffer d_b(context, begin(h_B), end(h_B), true);
cl::Buffer d_c(context, CL_MEM_WRITE_ONLY,
sizeof(float) * size);
cl::KernelFunctor
<int,cl::Buffer, cl::Buffer, cl::Buffer>
krow(program, "mmul");
zero_mat(N, h_C);
start_time = wtime();
krow(cl::EnqueueArgs(queue,
cl::NDRange(N, N)),
N, d_a, d_b, d_c);
run_time = wtime() - start_time;
cl::copy(queue, d_c, begin(h_C), end(h_C));
results(N, h_C, run_time);
}
int main(int argc, char *argv[])
{
std::vector<float> h_A, h_B, h_C; // matrices
int N; // A[N][N],B[N][N],C[N][N]
int i, err;
int size; // num elements in each matrix
double start_time, run_time; // timing data
cl::Program program;
N = ORDER;
size = N*N;
h_A = std::vector<float>(size);
h_B = std::vector<float>(size);
h_C = std::vector<float>(size);
initmat(N, h_A, h_B, h_C);
// Compile for first kernel to setup program
program = cl::Program(C_elem_KernelSource, true);
Context context(CL_DEVICE_TYPE_DEFAULT);
cl::CommandQueue queue(context);
std::vector<Device> devices =
context.getInfo<CL_CONTEXT_DEVICES>();
cl::Device device = devices[0];
std::string s =
device.getInfo<CL_DEVICE_NAME>();
std::cout << "\nUsing OpenCL Device ”
<< s << "\n";
krow(cl::EnqueueArgs(queue
cl::NDRange(N)),
N, d_a, d_b, d_c);
Changes to host program:
  1D ND Range set to number of rows in the C matrix

## Slide 128: Matrix multiplication performance
Matrices are stored in global memory.
Case | GFLOP/s | 
 | CPU | GPU
Sequential C (not OpenCL) | 0.85 | N/A
C(i,j) per work-item, all global | 111.8 | 70.3
C row per work-item, all global | 61.8 | 9.1
Third party names are the property of their owners.
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.
This hasn’t helped.
Device is NVIDIA® Tesla® P100 GPU with 56 compute units, 3,584 PEs
Device is 2x Intel® Xeon® CPU, E5-2695 v4 @ 2.1GHz

## Slide 129: Optimizing matrix multiplication
Notice that, in one row of C, each element reuses the same row of A.
Let’s copy that row of A from global memory into private memory of the work-item that’s (exclusively) using it, to avoid the overhead of loading it from global memory for each C(i,j) computation.
=
x
A(i,:)
B(:,j)
C(i,j)
Private memory of each work-item

## Slide 130: Matrix multiplication: OpenCL kernel (3/3)
__kernel void mmul(
const int N,
__global float *A,
__global float *B,
__global float *C)
{
int k, j;
int i = get_global_id(0);
float Awrk[1024];
float tmp;
for (k = 0; k < N; k++)
Awrk[k] = A[i*N+k];
for (j = 0; j < N; j++) {
tmp = 0.0f;
for (k = 0; k < N; k++)
tmp += Awrk[k]*B[k*N+j];
C[i*N+j] = tmp;
}
}
Setup a work array for A in private memory and copy into it from global memory before we start with the matrix multiplications.
(Actually, this is using far more private memory than we’ll have and so Awrk[] will be spilled to global memory)

## Slide 131: Matrix multiplication performance
Matrices are stored in global memory.
Case | GFLOP/s | 
 | CPU | GPU
Sequential C (not OpenCL) | 0.85 | N/A
C(i,j) per work-item, all global | 111.8 | 70.3
C row per work-item, all global | 61.8 | 9.1
C row per work-item, A row private | 9.6 | 24.9
Third party names are the property of their owners.
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.
Mixed, and still slower than naïve
Device is NVIDIA® Tesla® P100 GPU with 56 compute units, 3,584 PEs
Device is 2x Intel® Xeon® CPU, E5-2695 v4 @ 2.1GHz

## Slide 132: Why using too much private memory can be a good thing
In reality private memory is just hardware registers, so only dozens of these are available per work-item
Many kernels will allocate too many variables to private memory
  So the compiler already has to be able to deal with this
It does so by spilling excess private variables to (global) memory
You still told the compiler something useful – that the data will only be accessed by a single work-item
This lets the compiler allocate the data in such as way as to enable more efficient memory access

## Slide 133: Exercise: using private memory
Goal:
  Use private memory to minimize memory movement costs and optimize performance of your matrix multiplication program
Procedure:
  Start with your matrix multiplication solution
  Modify the kernel so that each work-item copies its own row of A into private memory
  Optimize step by step, saving the intermediate versions and tracking performance improvements
Expected output:
  A message to standard output verifying that the matrix multiplication program is generating the correct results
  Report the runtime and the MFLOPS

## Slide 134: Optimizing matrix multiplication
We already noticed that, in one row of C, each element uses the same row of A
Each work-item in a work-group also uses the same columns of B
So let’s store the B columns in local memory (which is shared by the work-items in the work-group)
=
x
A(i,:)
B(:,j)
C(i,j)
Private memory of each work-item
Local memory for each work-group

## Slide 135: Row of C per work-item, A row private, B columns local
__kernel void mmul(
const int N,
__global float *A,
__global float *B,
__global float *C,
__local float *Bwrk)
{
int k, j;
int i = get_global_id(0);
int iloc = get_local_id(0);
int nloc = get_local_size(0);
float Awrk[1024];
float tmp;
for (k = 0; k < N; k++)
Awrk[k] = A[i*N+k];
for (j = 0; j < N; j++) {
barrier(CLK_LOCAL_MEM_FENCE);
for (k=iloc; k<N; k+=nloc)
Bwrk[k] = B[k*N+j];
barrier(CLK_LOCAL_MEM_FENCE);
tmp = 0.0f;
for (k = 0; k < N; k++)
tmp += Awrk[k] * Bwrk[k];
C[i*N+j] = tmp;
}
}
Pass in a pointer to local memory. Work-items in a work-group start by cooperatively copying the columns of B they need into the work-group's local memory.

## Slide 136: Matrix multiplication host program (C++ API)
// Setup the buffers, initialize matrices,
// and write them into global memory
cl::Buffer d_a(context, begin(h_A), end(h_A), true);
cl::Buffer d_b(context, begin(h_B), end(h_B), true);
cl::Buffer d_c = cl::Buffer(context,
CL_MEM_WRITE_ONLY,
sizeof(float) * size);
cl::KernelFunctor<int, cl::Buffer, cl::Buffer,
cl::Buffer>
rowcol(program, “mmul”);
zero_mat(N, h_C);
start_time = wtime();
rowcol(cl::EnqueueArgs(queue, cl::NDRange(N)),
N, d_a, d_b, d_c);
run_time = wtime() - start_time;
cl::copy(queue, d_c, begin(h_C), end(h_C));
results(N, h_C, run_time);
}
int main(int argc, char *argv[])
{
std::vector<float> h_A, h_B, h_C; // matrices
int N; // A[N][N],B[N][N],C[N][N]
int i, err;
int size; // num elements in each matrix
double start_time, run_time; // timing data
cl::Program program;
N = ORDER;
size = N*N;
h_A = std::vector<float>(size);
h_B = std::vector<float>(size);
h_C = std::vector<float>(size);
initmat(N, h_A, h_B, h_C);
// Compile for first kernel to setup program
program = cl::Program(C_elem_KernelSource, true);
Context context(CL_DEVICE_TYPE_DEFAULT);
cl::CommandQueue queue(context);
std::vector<Device> devices =
context.getInfo<CL_CONTEXT_DEVICES>();
cl::Device device = devices[0];
std::string s =
device.getInfo<CL_DEVICE_NAME>();
std::cout << "\nUsing OpenCL Device ”
<< s << "\n";
Changes to host program: Pass local memory to kernels.
    This requires a change to the kernel argument lists … an arg of type LocalSpaceArg is needed.
    Allocate the size of local memory
    Update argument list in kernel functor
rowcol(cl::EnqueueArgs(queue, cl::NDRange(N)),
N, d_a, d_b, d_c, localmem);
cl::LocalSpaceArg localmem =
cl::Local(sizeof(float) * N);
cl::KernelFunctor<int, cl::Buffer, cl::Buffer,
cl::Buffer, cl::LocalSpaceArg>
rowcol(program, “mmul”);

## Slide 137: Matrix multiplication performance
Matrices are stored in global memory.
Case | GFLOP/s | 
 | CPU | GPU
Sequential C (not OpenCL) | 0.85 | N/A
C(i,j) per work-item, all global | 111.8 | 70.3
C row per work-item, all global | 61.8 | 9.1
C row per work-item, A row private | 9.6 | 24.9
C row per work-item, A private, B local | 12.3 | 55.4
Third party names are the property of their owners.
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.
Device is NVIDIA® Tesla® P100 GPU with 56 compute units, 3,584 PEs
Device is 2x Intel® Xeon® CPU, E5-2695 v4 @ 2.1GHz

## Slide 138: Exercise: using local memory
Goal:
  Use local memory to minimize memory movement costs and optimize performance of your matrix multiplication program
Procedure:
  Start with your matrix multiplication solution that already uses private memory from the previous exercise
  Modify the kernel so that each work-group collaboratively copies its own column of B into local memory
  Optimize step by step, saving the intermediate versions and tracking performance improvements
Expected output:
  A message to standard output verifying that the matrix multiplication program is generating the correct results
  Report the runtime and the MFLOPS

## Slide 139: Making matrix multiplication really fast
Our goal has been to describe how to work with private, local and global memory. We’ve ignored many well-known techniques for making matrix multiplication fast
  The number of work-items should be a multiple of the fundamental machine “vector width”. This is the wavefront on AMD, warp on NVIDIA, and the number of SIMD lanes exposed by vector units on a CPU
  To optimize reuse of data, you need to use blocking techniques
    Decompose matrices into tiles such that three tiles just fit in the fastest memory
    Copy tiles into local memory
    Do the multiplication over the tiles
  We have provided a very fast yet still quite simple block matrix multiply solution in OpenCL. This uses blocking with block sizes mapped onto the GPU’s warp/wavefront size. We'll come back to this later in the advanced section

## Slide 140: Matrix multiplication: sequential code
void mat_mul(int N, float *A, float *B, float *C)
{
int i, j, k;
for (i = 0; i < N; i++)
for (j = 0; j < N; j++)
for (k = 0; k < N; k++)
C[i*N+j] += A[i*N+k] * B[k*N+j];
}

## Slide 141: Matrix multiplication: sequential code
void mat_mul(int N, float *A, float *B, float *C)
{ // assume N % block_size = 0
int i, j, k;
int NB = N/block_size;
for (ib = 0; ib < NB; ib++)
for (i = ib*NB; i < (ib+1)*NB; i++)
for (jb = 0; jb < NB; jb++)
for (j = jb*NB; j < (jb+1)*NB; j++)
for (kb = 0; kb < NB; kb++)
for (k = kb*NB; k < (kb+1)*NB; k++)
C[i*N+j] += A[i*N+k]*B[k*N+j];
}
Break each loop into chunks with a size chosen to match the size of your fast memory

## Slide 142: Matrix multiplication: sequential code
void mat_mul(int N, float *A, float *B, float *C)
{ // assume N % block_size = 0
int i, j, k;
int NB = N/block_size;
for (ib = 0; ib < NB; ib++)
for (jb = 0; jb < NB; jb++)
for (kb = 0; kb < NB; kb++)
for (i = ib*NB; i < (ib+1)*NB; i++)
for (j = jb*NB; j< (jb+1)*NB; j++)
for (k = kb*NB; k < (kb+1)*NB; k++)
C[i*N+j] += A[i*N+k]*B[k*N+j];
}
Rearrange loop nest to move loops over blocks “out” and leave loops over a single block together

## Slide 143: Matrix multiplication: sequential code
void mat_mul(int N, float *A, float *B, float *C)
{ // assume N % block_size = 0
int i, j, k;
int NB = N/block_size;
for (ib = 0; ib < NB; ib++)
for (jb = 0; jb < NB; jb++)
for (kb = 0; kb < NB; kb++)
for (i = ib*NB; i < (ib+1)*NB; i++)
for (j = jb*NB; j< (jb+1)*NB; j++)
for (k = kb*NB; k < (kb+1)*NB; k++)
C[i*N+j] += A[i*N+k]*B[k*N+j];
}
This is just a local matrix multiplication of a single block

## Slide 144: Matrix multiplication: sequential code
void mat_mul(int N, float *A, float *B, float *C)
{ // assume N % block_size = 0
int i, j, k;
int NB = N/block_size;
for (ib = 0; ib < NB; ib++)
for (jb = 0; jb < NB; jb++)
for (kb = 0; kb < NB; kb++)
sgemm(C, A, B, …) // Cib,jb = Aib,kb * Bkb,jb
}
Note: sgemm is the name of the level three BLAS routine to multiply two matrices
=
x
A(ib,:)
B(:,jb)
C(ib,jb)

## Slide 145: Blocked matrix multiply: kernel
#define blksz 16
__kernel void mmul(
const unsigned int N,
__global float* A,
__global float* B,
__global float* C,
__local float* Awrk,
__local float* Bwrk)
{
int kloc, Kblk;
float Ctmp=0.0f;
// Compute element C(i,j)
int i = get_global_id(0);
int j = get_global_id(1);
// Element C(i,j) is in block C(Iblk,Jblk)
int Iblk = get_group_id(0);
int Jblk = get_group_id(1);
// C(i,j) is element C(iloc, jloc)
// of block C(Iblk, Jblk)
int iloc = get_local_id(0);
int jloc = get_local_id(1);
int Num_BLK = N/blksz;
// Upper-left-corner and inc for A and B
int Abase = Iblk*N*blksz; int Ainc = blksz;
int Bbase = Jblk*blksz; int Binc = blksz*N;
// C(Iblk,Jblk)=(sum over Kblk) A(Iblk,Kblk)*B(Kblk,Jblk)
for (Kblk = 0; Kblk<Num_BLK; Kblk++)
{
// Load A(Iblk,Kblk) and B(Kblk,Jblk).
// Each work-item loads a single element of the two
// blocks which are shared with the entire work-group
Awrk[jloc*blksz+iloc] = A[Abase+jloc*N+iloc];
Bwrk[jloc*blksz+iloc] = B[Bbase+jloc*N+iloc];
barrier(CLK_LOCAL_MEM_FENCE);
#pragma unroll
for (kloc=0; kloc<blksz; kloc++)
Ctmp+=Awrk[jloc*blksz+kloc]*Bwrk[kloc*blksz+iloc];
barrier(CLK_LOCAL_MEM_FENCE);
Abase += Ainc; Bbase += Binc;
}
C[j*N+i] = Ctmp;
}

## Slide 146: Blocked matrix multiply: kernel
#define blksz 16
__kernel void mmul(
const unsigned int N,
__global float* A,
__global float* B,
__global float* C,
__local float* Awrk,
__local float* Bwrk)
{
int kloc, Kblk;
float Ctmp=0.0f;
// Compute element C(i,j)
int i = get_global_id(0);
int j = get_global_id(1);
// Element C(i,j) is in block C(Iblk,Jblk)
int Iblk = get_group_id(0);
int Jblk = get_group_id(1);
// C(i,j) is element C(iloc, jloc)
// of block C(Iblk, Jblk)
int iloc = get_local_id(0);
int jloc = get_local_id(1);
int Num_BLK = N/blksz;
// Upper-left-corner and inc for A and B
int Abase = Iblk*N*blksz; int Ainc = blksz;
int Bbase = Jblk*blksz; int Binc = blksz*N;
// C(Iblk,Jblk)=(sum over Kblk) A(Iblk,Kblk)*B(Kblk,Jblk)
for (Kblk = 0; Kblk<Num_BLK; Kblk++)
{
// Load A(Iblk,Kblk) and B(Kblk,Jblk).
// Each work-item loads a single element of the two
// blocks which are shared with the entire work-group
Awrk[jloc*blksz+iloc] = A[Abase+jloc*N+iloc];
Bwrk[jloc*blksz+iloc] = B[Bbase+jloc*N+iloc];
barrier(CLK_LOCAL_MEM_FENCE);
#pragma unroll
for (kloc=0; kloc<blksz; kloc++)
Ctmp+=Awrk[jloc*blksz+kloc]*Bwrk[kloc*blksz+iloc];
barrier(CLK_LOCAL_MEM_FENCE);
Abase += Ainc; Bbase += Binc;
}
C[j*N+i] = Ctmp;
}
Load A and B blocks, wait for all work-items to finish
Wait for everyone to finish before going to next iteration of Kblk loop.
It’s getting the indices right that makes this hard

## Slide 147: Blocked matrix multiply: Host
#define DEVICE CL_DEVICE_TYPE_DEFAULT
int main(void)
{ // Declarations (not shown)
size = N * N; blksz = 16;
std::vector<float> h_A(size);
std::vector<float> h_B(size);
std::vector<float> h_C(size);
cl::Buffer d_A, d_B, d_C;
// Initialize matrices and setup
// the problem (not shown)
cl::Context context(DEVICE);
cl::Program program(context, util::loadProgram("mmul.cl", true));
cl::CommandQueue queue(context);
cl::KernelFunctor <int, cl::Buffer, cl::Buffer, cl::Buffer, cl::LocalSpaceArg, cl::LocalSpaceArg > mmul(program, "mmul");
d_A = cl::Buffer(context, begin(h_A), end(h_A),true);
d_B = cl::Buffer(context, begin(h_B), end(h_B),true);
d_C = cl::Buffer(context, CL_MEM_WRITE_ONLY, sizeof(float) * size);
cl::LocalSpaceArg Awrk =
cl::Local(sizeof(float) * blksz * blksz);
cl::LocalSpaceArg Bwrk =
cl::Local(sizeof(float) * blksz * blksz);
mmul(cl::EnqueueArgs( queue, cl::NDRange(N,N), cl::NDRange(blksz, blksz)), N, d_A, d_B, d_C, Awrk, Bwrk);
cl::copy(queue, d_C, begin(h_C), end(h_C));
// Timing and check results (not shown)
}

## Slide 148: Blocked matrix multiply: Host
#define DEVICE CL_DEVICE_TYPE_DEFAULT
int main(void)
{ // Declarations (not shown)
size = N * N; blksz = 16;
std::vector<float> h_A(size);
std::vector<float> h_B(size);
std::vector<float> h_C(size);
cl::Buffer d_A, d_B, d_C;
// Initialize matrices and setup
// the problem (not shown)
cl::Context context(DEVICE);
cl::Program program(context, util::loadProgram("mmul.cl", true));
cl::CommandQueue queue(context);
cl::KernelFunctor <int, cl::Buffer, cl::Buffer, cl::Buffer, cl::LocalSpaceArg, cl::LocalSpaceArg > mmul(program, "mmul");
d_A = cl::Buffer(context, begin(h_A), end(h_A),true);
d_B = cl::Buffer(context, begin(h_B), end(h_B),true);
d_C = cl::Buffer(context, CL_MEM_WRITE_ONLY, sizeof(float) * size);
cl::LocalSpaceArg Awrk =
cl::Local(sizeof(float) * blksz * blksz);
cl::LocalSpaceArg Bwrk =
cl::Local(sizeof(float) * blksz * blksz);
mmul(cl::EnqueueArgs( queue, cl::NDRange(N,N), cl::NDRange(blksz, blksz)), N, d_A, d_B, d_C, Awrk, Bwrk);
cl::copy(queue, d_C, begin(h_C), end(h_C));
// Timing and check results (not shown)
}
One work-item per element of the C matrix organized into 16 by 16 blocks.
Setup local memory with blocks of A and B (16 by 16) that should fit in local memory.

## Slide 149: Matrix multiplication performance
Matrices are stored in global memory.
Case | GFLOP/s | 
 | CPU | GPU
Sequential C (not OpenCL) | 0.85 | N/A
C(i,j) per work-item, all global | 111.8 | 70.3
C row per work-item, all global | 61.8 | 9.1
C row per work-item, A row private | 9.6 | 24.9
C row per work-item, A private, B local | 12.3 | 55.4
Block oriented approach using local | 138.0 | 1,801.8
Third party names are the property of their owners.
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.
P100 peak is ~8.5 TFLOP/s single precision.
E5-2695 peak is ~1.2 TFLOP/s s.p.
Device is NVIDIA® Tesla® P100 GPU with 56 compute units, 3,584 PEs
Device is 2x Intel® Xeon® CPU, E5-2695 v4 @ 2.1GHz
11.5% of peak
21.2% of peak
Notes: E5-2695 v4 @ 2.1GHz FLOP/s calc is 2.1GHz * 16 ops/cycle (AVX 2 256-bit FMA 32-bit) * 36 cores = 1,209.6 GFLOP/s
P100 FLOP/s calc is 1.189GHz * 3584 (PEs) * 2 (FMA) for FP32, half for FP64
James’ comments about the P100s in Isambard:
”NVIDIA's published clock speeds for our cards (16GB HBM2, PCIe version) are 1126 base and 1303 boost, which gives 8071 or 9340 GFLOP/s FP32 (these are the same numbers listed in Wikipedia).
Running `nvidia-smi` on the cards shows a 1189 base and boost 1328, which gives 8523 or 9519 GFLOP/s FP32. These numbers do not match any published numbers that I can find.”

## Slide 150: Matrix multiplication performance
Block sizes are crucial to performance
Case | GFLOP/s | 
 | CPU | GPU
Block oriented approach using local, 8x8 | 67.5 | 1,511.3
Block oriented approach using local, 16x16 | 109.6 | 1,801.8
Block oriented approach using local, 32x32 | 134.9 | 1,796.0
Block oriented approach using local, 64x64 | 138.0 | N/A
Vendor SGEMM (MKL / NVIDIA CuBLAS) |  | 
Third party names are the property of their owners.
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.
Device is NVIDIA® Tesla® P100 GPU with 56 compute units, 3,584 PEs
Device is 2x Intel® Xeon® CPU, E5-2695 v4 @ 2.1GHz

## Slide 151: Matrix multiplication performance (CPU)
Matrices are stored in global memory.
Case | MFLOPS
 | CPU
Sequential C (not OpenCL, compiled /O3) | 224.4
C(i,j) per work-item, all global | 841.5
C row per work-item, all global | 869.1
C row per work-item, A row private | 1,038.4
C row per work-item, A private, B local | 3,984.2
Block oriented approach using local (blksz=8) | 7,482.5
Block oriented approach using local (blksz=16) | 12,271.3
Block oriented approach using local (blksz=32) | 16,268.8
Intel MKL SGEMM | 63,780.6
Device is Intel® Core™ i5-2520M CPU @2.5 GHz (dual core) Windows 7 64 bit OS, Intel compiler 64 bit version 13.1.1.171, OpenCL SDK 2013, MKL 11.0 update 3.
Third party names are the property of their owners.
These are not official benchmark results. You may observe completely different results should you run these tests on your own system.
Notes: For the Tesla system described on this slide, here are the performance numbers with the actual programs used in the tutorial
Solution 05 --- Parallel matrix mult (dot prod), order 1024 on CPU ==0.57 seconds at 3734.8 MFLOPS
Solution 06---Parallel matrix mult (dot prod), order 1024 on CPU = 0.52 seconds at 4114.0 MFLOPS
Solution 07-----Parallel matrix mult (dot prod), order 1024 on CPU = 0.26 seconds at 8259.6 MFLOPS
Solution 08--- Parallel matrix mult (dot prod), order 1024 on GPU = 0.27 seconds at 7837.5 MFLOPS
Solution 09 --Parallel matrix mult (dot prod), order 1024 on GPU = 0.03 seconds at 67108.9 MFLOPS

## Slide 152: Exercise: blocked matrix multiply
Goal:
  To understand the effect of changing certain parameters in an optimised matrix multiply code.
Procedure:
  Start from the provided blocked matrix multiplication program.
    cd ~/opencl-training/solutions/MatMul
  Measure the performance of the code as provided.
  Modify parameters such as the block sizes, overall problem size etc. and measure what happens to the performance.
Expected output:
  Test your result and verify that it is correct. Output the runtime and the GFLOP/s. What's the highest performance you can achieve?
Extra: try using NVIDIA CuBLAS or Intel MKL

## Slide 153: Synchronization in OpenCL

## Slide 154: Consider N-dimensional domain of work-items
Global Dimensions:
  1024x1024 (whole problem space)
Local Dimensions:
  128x128 (work-group, executes together)
Synchronization: when multiple units of execution (e.g. work-items) are brought to a known point in their execution. The most common example is a barrier … i.e. all units of execution “in scope” arrive at the barrier before any are allowed to proceed.
1024
1024
Synchronization between work-items possible only within work-groups:
barriers and memory fences
Cannot synchronize between work-groups within a kernel

## Slide 155: Where might we need synchronization?
Consider a reduction … reduce a set of numbers to a single value
  E.g. find sum of all elements in an array
Sequential code
int reduce(int Ndim, int *A)
{
int sum = 0;
for (int i = 0; i < Ndim; i++)
sum += A[i];
return sum;
}

## Slide 156: Simple parallel reduction
A reduction can be carried out in three steps:
  Each work-item sums its private values into a local array indexed by the work-item’s local id
  When all the work-items have finished, one work-item sums the local array into an element of a global array (indexed by work-group id).
  When all work-groups have finished the kernel execution, the global array is summed on the host.
Note: this is a simple reduction that is straightforward to implement. More efficient reductions do the work-group partial reductions in parallel on the device rather than on the host. These more scalable reductions are considerably more complicated to implement.

## Slide 157: A simple program that uses a reduction
Numerical Integration
Mathematically, we know that we can approximate the integral as a sum of rectangles.
Each rectangle has width and height at the middle of interval.
F(x) = 4.0/(1+x2)
4.0
2.0
1.0
X
0.0

## Slide 158: Numerical integration source code
The serial Pi program
static long num_steps = 100000;
double step;
void main()
{
int i; double x, pi, sum = 0.0;
step = 1.0/(double) num_steps;
for (i = 0; i < num_steps; i++) {
x = (i+0.5)*step;
sum = sum + 4.0/(1.0+x*x);
}
pi = step * sum;
}

## Slide 159: Exercise 8: The Pi program
Goal:
  To understand synchronization between work-items in the OpenCL C kernel programming language
Procedure:
  Start with the provided serial program to estimate Pi through numerical integration
  Write a kernel and host program to compute the numerical integral using OpenCL
  Note: You will need to implement a reduction
  Reduction examples are included in AMD and Nvidia's OpenCL SDKs
Expected output:
  Output result plus an estimate of the error in the result
  Report the runtime
Hint: you will want each work-item to do many iterations of the loop, i.e. don’t create one work-item per loop iteration. To do so would make the reduction so costly that performance would be terrible.